## Slide 1: Netfilter를 이용한 packet capturing

## Slide 2: Setting testing environment
Download and setup linux kernel

## Slide 3: Network device driver

## Slide 4: Internet protocol in Linux
ip_input.c
ip_rcv
ip_forward.c
Higher Layers
dev.c
net_rx_action
ip_rcv_finish
IP_PRE_ROUTING
ip_forward
ip_forward_finish
ip_local_deliver
IP_LOCAL_INPUT
ip_local_deliver
IP_FORWARD
ip_output.c
ip_finish_output2
dev.c
ip_output
IP_POST_ROUTING
ip_queue_xmit2
IP_LOCAL_OUTPUT
ip_queue_xmit
ip_finish_output
dev_queue_xmit
ip_fragment

## Slide 5: Socket buffer
skb (Linux Socket buffer)‏
  Buffers in which linux kernel handles network packets
    Packet is received by network card, put into a skbuff and then passed to the network stack
    Packet data and management information
    The sk_buff is first incomplete, then filled in during passage through the kernel, both for received packets and for sent packets
    커널 내의 다양한 네트워크 계층을 지나감에 따라 완성되는 패킷 구조체

## Slide 6: sk_buff structure

## Slide 7: Review of network device driver & packet capturing
Capture the packet!!

## Slide 8: Makefile
obj-m := drop.o
all:
make -C /lib/modules/$(shell uname -r)/build M=$(PWD) modules

## Slide 9: drop.c
#include <linux/module.h>
#include <linux/skbuff.h>
#include <linux/netdevice.h>
#include <linux/netfilter.h>
#include <linux/netfilter_ipv4.h>
#include <linux/in.h>
#include <linux/tcp.h>
#include <linux/udp.h>
#include <linux/ip.h>
static struct nf_hook_ops netfilter_ops;
struct sk_buff *sock_buff;
unsigned long inet_aton(const char*);

## Slide 10: drop.c
unsigned int main_hook(unsigned int hooknum, struct sk_buff *skb,
const struct net_device *in,
const struct net_device *out,
int (*okfn)(struct sk_buff*))
{
struct iphdr *iph = ip_hdr(skb);
unsigned long saddr = 0, daddr = 0;
unsigned short sport = 0, dport = 0;
struct tcphdr *tcph = (struct tcphdr*)tcp_hdr(skb);
unsigned long cse = inet_aton("164.125.7.52");
saddr = iph->saddr;
daddr = iph->daddr;
if(saddr == cse){return NF_DROP;}
return NF_ACCEPT;
}

## Slide 11: drop.c
int init_module()
{
netfilter_ops.hook = main_hook;
netfilter_ops.pf = PF_INET;
netfilter_ops.hooknum = NF_INET_PRE_ROUTING;
netfilter_ops.priority = 1;
nf_register_hook(&netfilter_ops);
return 0;
}
void cleanup_module()
{
nf_unregister_hook(&netfilter_ops);
}

## Slide 12: drop.c
unsigned long inet_aton(const char * str)
{
unsigned long result = 0;
unsigned int iaddr[4] = {0,};
unsigned char addr[4] = {0,};
int i;
sscanf(str,"%d.%d.%d.%d ",iaddr,iaddr+1,iaddr+2,iaddr+3);
for(i = 0 ; i < 4 ; i++)
addr[i] = (char)iaddr[i];
for(i = 3 ; i > 0 ; i--)
{
result |= addr[i];
result <<= 8;
}
result |= addr[0];
return result;
}

## Slide 13: Compile & insert module

## Slide 14: Test your simple firewall!

## Slide 15: IP header

## Slide 16: iphdr structure
/linux/ip.h
struct iphdr {
…
__u32 saddr;
__u32 daddr;
};

## Slide 17: TCP header

## Slide 18: tcphdr structure
/linux/tcphdr
struct tcphdr {
unsigned short source;
unsigned short dest;
...
};

## Slide 19: Homework
방화벽 다시 만들어 보기
포트 체크 기능 추가 – FTP/SSH 포트 막아보기